The QF2-pre Guide
Dr. John A. Jones

Questions / Corrections / Requests? - Email: qf2-pre@jxj.me.uk

THIS DOCUMENT IS INTENDED TO MATCH THE LATEST VERSION MENTIOEND IN THE REVISION HISTORY. THERE IS NO GUARANTEE THAT ANY OTHER FIRMWARE VERSION WILL MATCH THIS DOCUMENT.

If you are using a firmware listed in the revision history, the python tools will identify the firmware loaded in the QF2-pre over the network, and will attempt to provide consistent behavior for the end user no matter which version is in use. It is possible that features may not be available in different firmware / tool revisions, so you may need to update the firmware and / or software to a particular revision to use a feature. If you attempt to use a feature that is unavailable, the Python tools will throw an exception.

If in doubt, you can go here to get the latest tagged release of tools, firmware and examples:

https://gitlab.com/qf2-pre/users/tags

Revision History

2018-2-7

git tag: v0.55_unstable
Bootloader SHA256: N/A
Bootloader build date: N/A
Runtime SHA256: N/A
Runtime build date: N/A

Test version.

2018-2-7

git tag: v0.56_unstable
Bootloader SHA256: N/A
Bootloader build date: N/A
Runtime SHA256: N/A
Runtime build date: N/A

Test version.

2018-3-6

git tag: v0.57_unstable
Bootloader SHA256: 087832b8557b2d9fe13080644ae25e02dbe3d618ae837e0054342860cf60bc80
Bootloader build date: 1517338548 (2018-01-30 18:55:48)
Runtime SHA256: 511fdfdb51090fea1bdc3de976beca644ec045542c5933c67babb65519f3160a
Runtime build date: 1520372952 (2018-03-06 21:49:12)

First complete version. Added automatic Kintex-7 boot.

2018-3-21

git tag: v0.58_unstable
Bootloader SHA256: bcdc9d2417e4c039838d254701efe39326368f2215fe2267938419470c4465fa
Bootloader build date: 1520961844 (2018-03-13 17:24:04)
Runtime SHA256: f1b81b50d9c72fe47970310e451e09c1e32477d6d4b353ddff5f215c74228238
Runtime build date: 1521496662 (2018-03-19 21:57:42)

Comments: Support added for SL25FL-L PROM (bootloader was updated as well). Configuration system updated to support JSON parsing as well as settings lists – checks against firmware on PROM to verify compatibility. Updating firmware will now automatically migrate the configuration on the PROM. Monitoring can now be disabled. Fixed minor bug on TAS2505 reset pin (only for development at the moment). Fixed issue with missing ntplib causing failure of firmware update (now ignores error and uses local clock).

2018-5-18

git tag: v0.59_unstable
Bootloader SHA256:
Bootloader build date:
Runtime SHA256:
Runtime build date:

update_spartan_6_image now automatically migrates the configuration space from the previous firmware by default. Ethernet core now monitors the PHY to verify connection before allowing communication – fixes an issue with the PHY where it won’t establish a link unless no data is being sent during negotiation. PWM control is now available for the ATX fan. Packet disruption by a misbehaving Kintex-7 FPGA is now less likely to affect operation. The bootloader now includes monitoring. The bootloader now ensures main power is switched off after load. The board UID is now part of the information payload on port 50000, and is queried automatically at startup. Ethernet link negotiation time is now smaller due to MDIO cable detect. Standard QSFP registers are monitored automatically as part of the runtime monitoring system. Known issue: the I2C error latch is always ‘1’ due to QSFP detection using I2C.

2020-1-14

git tag: 0.7.0+0
Bootloader SHA256:
Bootloader build date:
Runtime SHA256:
Runtime build date:

Changes:

- Fiber ethernet support.
- Bootloader PROM data can be write-protected.
- 1Gb/s self-training 8b10b link between Kintex-7 & Spartan-6.
- Rebooting to bootloader via software or recovery button now disables AUTOBOOT_TO_RUNTIME.
- The runtime is no longer allowed to reboot to itself, only to the bootloader.
- The SI570s can now be programmed by requested frequency, and the Spartan-6 monitors their current frequency.
- Experimental SD card access.
- Experimental microphone recording.
- Experimental humidity, B-field, gyro, accelerometer, air pressure data.
- Experimental speaker & headphone.

Known Issues / Limitations

- FMC sites are 'swapped', and therefore incompatible with some double FMCs (i.e. the HPC FMC should be the top site, and the LPC the bottom). This was a known consequence of the Kintex-7 FPGA banking.

- Some virtual channels between the Spartan-6 and Kintex-7 are not yet implemented.

1 – Hardware

1.1 - Overview

The QF2-pre is a double FMC carrier. It has one HPC mezzanine site, and one LPC site. The total FMC I/O count is 228 lines. Both are fully allocated aside from the serial links, which are unused. There are two FPGAs on the board:

A Spartan-6 LX45T is used to provide the core functions of the board. It implements a boot system, ethernet communications (ARP, PING, UDP & IP MULTICAST), power management and power supply clock phasing and board monitoring. It has a non-volatile configuration space in its PROM, and maintains several Kintex-7 firmwares which can be loaded automatically at boot. The Spartan-6 also manages the FMC and QSFP I2C interfaces and the FMC JTAG interfaces and dedicated clocks.

A Kintex-7 160T / 325T is used as an application FPGA. It is mostly dedicated to interfacing to the FMCs and MFCs.

The two FPGAs are connected by a full-duplex, flow-controlled, LVDS link with a CRC-32 checksum and packet re-transmit operating at a 1Gb/s line rate. It is encoded using 8b10b, giving an effective data rate of 800Mb/s. The separation of functionality between the FPGAs significantly reduces the overhead in the Kintex-7 firmware as e.g. network interfaces are already implemented in the Spartan-6, and ensures the board is always up and cannot be 'bricked'.

The system operates with a standard clock of 50MHz, derived from a 25MHz local oscillator connected to the Spartan-6 FPGA.

The board has a modular power system, with independent supplies for the Spartan-6, Kintex-7 and FMCs, which allows the board to power on and off in stages while maintaining communication with a host over ethernet. The FMC VADJ supply voltages are digitally programmable, but are currently locked in the firmware at +1.8V for the HPC FMC (Kintex-7 HP I/O) and +2.5V for the LPC FMC (Kintex-7 HR I/O), supporting LVDS by default.

1.2 – Design Philosophy

FPGA technology (and electronics in general) have become a great deal more complicated over the past decade. This puts many of the device features outside the expertise of the layperson, or many more experienced designers who are too busy to spend time understanding them. This board was in part designed to combat these issues while still providing high performance at a reasonable price point.

The governing philosophy of its design is:

Ensure mistakes are in-system recoverable: The Spartan-6 firmware has a bootloader that is optionally write-protected in hardware, a highly recommended practice for inaccessible systems. As such, even a complete corruption can be recovered from by power-cycling to return to the bootloader.

Provide communications and diagnostic interfaces to support development and testing: Often when we develop a new application firmwares, a lot of effort is expended developing as stable communication interface to the board. Further, it can be a challenge to identify whether faults are at the hardware-level or in the new firmware. To avoid this, many diagnostic features are implemented in the Spartan-6 FPGA. Their output (which has been field-tested and verified) can be cross-checked against the user’s application firmware to identify issues during development. In addition, a Kintex-7 demonstration firmware and software framework is provided to help aid in identifying hardware faults.

Make it as easy as possible for a user to access the powerful features of the hardware without writing doing everything from scratch: Many of the QF2-pre features such as board monitoring, power supply phasing, remote programming and debug, over temperature shutdown, protected bootloader, etc... are available via a simple python interface. They are managed by the Spartan-6 FPGA, so you don’t have to write any firmware to use them, and you aren’t at risk of breaking them when you develop your application firmware.

Conversely, allow for power users to access the raw data: Perhaps you don’t want to use the features in the Spartan-6 firmware, or want to do something slightly different to the typical user such as implementing network protocols that the Spartan-6 doesn’t support. This can be achieved by using bypass controls built into the Spartan-6 runtime that will forward the ‘raw’ data for different features to the Kintex-7.

If there is something you think this board isn’t capable of but should be, we’d be interested in hearing about it – hopefully it’s something that can be incorporated into later revisions of firmware (or if necessary, hardware) for the benefit of all. The firmware and hardware design are derived from experiences in many projects and progressively improved, so that every current and future user can benefit. Backward-compatibility is maintained whenever possible, or an equivalent feature provided otherwise.

The core Spartan-6 firmware is currently closed-source. The main reason for this is to maintain the critical infrastructure of the board with a clean development and test cycle. The Spartan-6 firmware is non-trivial, and it is important for all users that any issues can be easily recognized and addressed. The Spartan-6 firmware contains several diagnostic features which aid in the recovery of malfunctioning hardware and understanding what went ‘wrong’. If multiple firmware variants written by users were running in the field, it would be impossible for us to provide effective technical support.

1.2 - Hardware Feature Summary

1.2.1 – Application Resources

- Kintex-7 160T / 325T FPGA.
- Eight 10.3Gb/s serial links to application FPGA via QSFP+.
- External RF 50-ohm GTX transceiver clock input via U.FL connector.
- Dedicated 125MHz MEMS oscillator for Kintex-7 serial links.
- One fully populated (except serial links) HPC FMC with programmable VADJ (typically +1.8V).
- One fully populated (except serial links) LPC FMC with programmable VADJ (typically +2.5V).
- Two Hirose FH29 ZIF connectors connected to Kintex-7 HR banks with VCCO @ +2.5V (v1.5 ONLY).
- Two Samtec ZRAY connectors connected to Kintex-7 HR banks with VCCO @ +2.5V (v1.6 ONLY).
- Two orange LEDs.
- Independent main power system.

1.2.2 – Shared Resources

- Two reconfigurable SI570 oscillators for serial links (shared to both Kintex-7 and Spartan-6 FPGAs). Default startup frequency is 156.25MHz.

1.2.3 – System Resources

- Supply voltage +6V - +14.5V.
- Spartan-6 LX45T system FPGA.
- Dedicated 125MHz oscillator for Spartan-6 serial links.
- Gigabit Ethernet over copper and Fiber Ethernet support via QSFP.
- uSD card.
- PDM microphone.
- Supply voltage, supply current, ambient humidity, barometric pressure and magnetic field monitoring.
- Recovery, diagnostic and user-defined push buttons with jumper bypass for chassis switches.
- Board and device temperature montoring, with automatic thermal overload protection for Kintex-7 FPGA, independent of internal XADC.
- Atmel cryptographic security chip (key authentication, certificates, unique ID, TRNG, OTP memory).
- 256Mb boot PROM with write-protected bootloader.
- 9-axis IMU.
- Speaker and headphone socket.
- ATX fan header with tach & PWM support.
- Four tri-colour LEDs.

1.3 - Spartan-6 Protected Bootloader & Runtime Firmwares

There are two versions of the Spartan-6 firmware: a protected bootloader firmware and a runtime firmware.

The bootloader is a simplified Spartan-6 firmware that resides in the first 32 x 64kB sectors of the on-board PROM. It always loads before anything else and contains the following components:

- Copper & fiber ethernet support with non-volatile network settings stored in the PROM.
- A system I2C controller that ensures the board is in a known state with main power turned off, and provides monitoring information.
- A programming interface for the on-board PROM.
- A variety of diagnostic & testing interfaces for e.g. audio, SD access and PMOD I/O.
- An ICAP reboot controller that can trigger a reload of the Spartan-6 firmware.

The firmware is complete enough to allow reconfiguration of the runtime image of the Spartan-6 and to trigger reloading into the image. As such, it can provide a protected fail safe in the event of a corrupted runtime firmware. The PROM settings for the bootloader and runtime are independent from each other.

For normal operation, the board can be started either by loading the bootloader and waiting for a user command via Ethernet to load the runtime firmware, or by automatically jumping to the runtime firmware immediately. The mode in use is determined by the bootloader register settings.

NOTE: In situations where the recovery mode button is typically inaccessible, it is highly recommended that the bootloader is configured to await an external command before entering into the runtime firmware and that the lower 32 sectors of the PROM are write-protected. This will allow the board to be recovered by power-cycling in the event of a corrupted runtime configuration, as the bootloader network settings and firmware are completely independent of the runtime.

NOTE: By default, once the write-protect for the PROM has been enabled in software, it cannot be disabled again without physically applying a jumper to the header next to the Spartan-6.

Irrespective of the mode the bootloader is configured in, it can be also be forced into a recovery mode using the bootloader firmware by holding down the recovery mode button before power is applied to the board, or similarly using an external switch attached to the appropriate jumper (for cases where e.g. the board is mounted in a chassis). This will force the bootloader to use it’s default register and network settings and disable automatic reboot into the runtime firmware. This is further documented in the recovery mode section below.

The runtime firmware contains all the additional features documented below in addition to those of the bootloader.

1.4 - Copper and Fiber Ethernet Support

The current Spartan-6 firmware supports copper ethernet operating at 1Gb/s using a Micrel KSZ9031RNX RGMII PHY. The firmware implementation is gigabit-only and does not work at 10Mb/s or 100Mb/s interface speeds.

In addition, the firmware supports 4-channel fiber Ethernet. The current implementation multiplexes these channels, providing redundancy in the case of e.g. a damaged fiber. The chosen fiber is selected using the NETWORK_INTERFACE parameter, and as with other network settings, the interface will only change on reboot.

The Spartan-6 ethernet interface has a UDP ethernet core which eliminates some of the network firmware infrastructure required in the Kintex-7. It supports:

- ARP
- ICMP PING.
- A single multicast UDP channel that is forwarded to the Kintex-7 FPGA. It does not support registration, which must be statically configured in the attached network.
- UDP echo on port 7.
- Board identification on UDP port 50000.
- Spartan-6 configuration space on UDP port 50001.
- External system I2C interface on port 50002.
- Kintex-7 / FMC JTAG & PROM SPI sequencer on port 50003.
- Kintex-7 UDP port forwarding over ports 50004 – 50007 (available ONLY in runtime).

All data channels operate by sending / receiving UDP packets to / from these ports. DHCP and TCP are not currently supported.

A channel multiplexer in the Spartan-6 separates the streams and records the source UDP port and source IP for each channel separately, and sends subsequent responses to that target after receiving each request. Therefore, each individual channel can can have an independent master, but a single channel must only have one. The architecture is designed so that most single-packet transactions are atomic. Therefore a board is recoverable even in the event two masters collide.

As the QF2-pre is fundamentally a slave device, it has no concept of subnets (or need for them) and simply sends packets to the last master on a given port that it received a packet from.

Keeping the channels separate allows one to for example run a Xilinx Chipscope interface to the Kintex-7 on port 50002 using the included Xilinx Virtual Cable interface script, while operating the board normally using the other channels.

The PROM / JTAG interface is stable, and is forward and backward compatible with past and future Spartan-6 firmwares.

1.5 - Board LEDs

The board has six standard LEDs. Two are located near the ZIF (v1.5) / ZRAY (v1.6) sockets near the top of the board and are connected to the Kintex-7. The other four are connected to the Spartan-6 and are located at the four corners of the board. The Kintex-7 LEDs emit orange light, and the Spartan-6 LEDs are tri-color and can therefore produce colors across the visible spectrum.

1.5.1 Kintex-7 LED Interpretation

Kintex-7 LED usage is application-specific. They emit orange light.

1.5.2 Spartan-6 Bootloader LED Interpretation

The default interpretation of the Spartan-6 LEDs is shown below. It is possible to transfer control of these LEDs to the Kintex-7 FPGA using a virtual communication channel, as described later in this document.

Top-left (by headphone socket):

Red: PROM configuration checksum failure - using default network settings.
Blue: Recovery mode - using default network settings.
Green: PROM configuration checksum pass - using PROM network settings.

NOTE: Depending on whether the recovery mode button was depressed during firmware load or afterwards, the firmware settings will either be the defaults or those stored in the PROM (if valid).

Bottom-left (by ethernet socket):

Flashing red: Spartan-6 programmed.
Blue: UDP ethernet transaction in progress.

Top-right (by top FMC):

Pink: Indicates bootloader firmware.

Bottom-right (by bottom FMC):

Pink: Indicates bootloader firmware.

1.5.3 Spartan-6 Runtime LED Interpretation

Top-left (by headphone connector):

Red: PROM configuration checksum failure - using default firmware and default network settings.
Green: PROM configuration checksum pass - using PROM settings.

Bottom-left (by ethernet connector):

Flashing green: Spartan-6 programmed.
Flashing blue: UDP ethernet transaction in progress.

Top-right (by top FMC):

Application-specific – controlled by the Kintex-7 through a virtual channel.

Bottom-right (by bottom FMC):

Application-specific – controlled by the Kintex-7 through a virtual channel.

1.6 - High-Performance Clocking

There are four different high-performance clock sources on the board. These clocks are solely for the purpose of driving the serial links on the Kintex-7 and Spartan-6. Usage of an appropriate source depends on a user's application. The four sources are:

Local oscillator (SiTime MEMS oscillator): This can be populated by either a SIT912X one-time programmable oscillator (+3.3V, LVDS), or a SiTime DCXO. The Spartan-6 and Kintex-7 each have a separate oscillator site which is by default fitted with a 125MHz SIT9121 (alternative values can be fitted on request).

Pros: Easy to use, low power.
Cons: Frequency is one-time programmable.

External clock: A dedicated 50-ohm RF clock can be provided directly to the Kintex-7 via a U.FL connector.

Pros: Simple to use, useful for test and characterization, can be used to synchronize to a global system clock.
Cons: Requires a high-quality reference to be provided off-board.

SI57X programmable oscillators / VCXO: These generate programmable frequency references which can also be manipulated dynamically over I2C at up to 10kHz for frequency tracking applications. They are configured over I2C via the Spartan-6. The settings are part of the Spartan-6 configuration data and the devices can be automatically enabled at startup.

Pros: Programmable frequency, can be used to track a reference.
Cons: Relatively complex to configure and operate.

1.7 – Board Health Monitoring

The QF2-pre provides many options for monitoring the board health of the system. It monitors all the supply voltages on the board, and the current consumption of all the primary switching regulators. It also has an ATX fan header which is capable of PWM modulation and fan speed (tachometer) measurement. The humidity sensor can be e.g. used to detect the presence of water in the electronics environment from e.g. a faulty cooling system. Barometric pressure sensing, tri-axis magnetic field sensing and a 9-axis IMU are also included.

All the available board monitoring devices are polled by the Spartan-6 (in both bootloader and runtime firmwares) at ~2.6 second intervals. This interval cannot be changed by the user and represents a compromise between responding to events promptly and excessive polling of the system I2C bus.

The monitoring data can be read back from the Spartan-6 configuration space.

1.8 – Over Temperature Shutdown

In order to protect the hardware from excessive temperatures (and in particular the Kintex-7 FPGA), the Spartan-6 runtime firmware features an over-temperature shutdown feature. The Spartan-6 will turn off all the main power regulators on the board if the temperature of the Kintex-7 FPGA exceeds a programmable threshold (the default is 80C). There is a separate threshold for the board temperature (the default is 80C).

In addition to this, it is highly recommended that the internal over-temperature shutdown feature of the Kintex-7 FPGA is enabled to provide an extra layer of safety.

1.9 – Audio Interface & Diagnostic Audio Output

For situations where the network settings of a board are unknown and recovery mode is undesirable, or diagnostic information is desired but a computer is unavailable, the diagnostic mode button can be used. Pressing it will trigger an audio output on the on-board speaker, or via a pair of headphones if they are plugged in, providing information about the current board status.

The audio output provides information on the current IP and MAC address of the board.

The Kintex-7 can also drive audio output using a virtual channel in the Kintex-Spartan link. The audio stream is encoded using single-channel 16-bit PCM at 44.1kHz. This link is always available and does not need to be enabled in the Spartan-6.

If the diagnostic button is pressed while the Kintex-7 is streaming data, the Kintex-7 channel is back-pressured until the diagnostic output is complete, and will then resume its previous operation.

1.10 – PDM Microphone Input

The data from the PDM microphone attached to the Spartan-6 is available to the Kintex-7 using a virtual channel. The master enable for the channel must be enabled in the Spartan-6 configuration, after which it the control of the PDM microphone output is handed off to the Kintex-7. The Kintex-7 can then turn on / off the microphone using a control signal sent over the Kintex-Spartan link.

The raw output from the PDM microphone is 1-bit at 2.8224MHz. As this isn’t generally useful for audio applications, the data is processed in the Spartan-6 via a 5th order CIC filter with a decimation of 64, giving a cutoff around 20kHz. The microphone response is very uniform up to 10kHz then rolls off steeply. A post-compensating FIR filter is not currently used.

The resulting data sent to the Kintex-7 is in single-channel, 16-bit, 44.1kHz PCM format.

1.11 – FMC and QSFP I2C Access

The I2C interfaces for the FMC sites and QSFPs are shared with the system I2C bus via a multiplexer. There are two ways they can be accessed:

- A diagnostic interface in the Spartan-6 which is accessible using the example Python code below.
- The monitoring system can automatically read standard QSFP registers during the polling loop.

2.0 – Usage

2.1 – Turning the Board on for the First Time

If you are receiving a new board, you should find that the PROM is already programmed with firmware and settings that match the firmware defaults.

To begin with one should apply power to the board either using a supply jack (center positive) or the header terminals.

Once power is applied, the board LEDs should flash red by the Ethernet connector (indicating the bootloader is running on the Spartan-6) and the LED by the headphone jack should be green, indicating the board is using the PROM configuration settings. Other behaviors can happen if the board has already been user-configured, so if you see something else, consult the LED section.

The board should be connected to a network-capable computer with a static IPv4 address in the 192.168.1.X subnet, initially via the copper interface as the optical interface is disabled by default. Communicating with the board over Ethernet involves targeting the IP address 192.168.1.127. The board’s MAC address is set to AA:BB:CC:DD:EE:FF by default. A simple test would be to ping the board using that IP to ensure communication is established before using other scripts / tools.

NOTE: It is recommended that a minimum of a 15W power supply is used, as the use of all the board features (in particular the serial links and QSFPs) will demand too much from lesser supplies and may create undesired / unexpected behavior. The supply voltage is user-defined between +6V and +14.5V, but be aware that the FMC standard expects a +12V rail, so the user should check that any FMCs are compatible with non-standard voltages before use. Lower supply voltages will increase the overall efficiency of the board power system and therefore decrease board power dissipation.

2.2 – Recovery Mode

There are two ways a board will definitely start up with all default settings:

- If the PROM settings are corrupted or not set the bootloader will fail to detect a valid checksum (verified using the Fletcher-16 algorithm) and will use its default settings instead.
- The user presses the recovery button down just before the end of the initial 3s reset cycle (before the LED by the RJ-45 connector is flashing), then releases it immediately afterwards (holding it for longer will trigger a firmware reboot).

There are several ways of using the recovery button:

Holding the button down before and during power-up: This will load the bootloader firmware and force the Spartan-6 bootloader to use its default settings, which will prevent it from automatically launching the runtime firmware. It will also reset the IP address to 192.168.1.127 and MAC address to AA:BB:CC:DD:EE:FF.

Depressing for fewer than approximately three seconds, then releasing the recovery button: This will alternate between using the PROM network settings and the firmware defaults while the bootloader firmware is running.

Depressing for more than approximately three seconds, then releasing the recovery button: This will trigger a reboot of the Spartan-6 into the bootloader firmware irrespective of which firmware is currently running in the Spartan-6. The PROM settings still be used if the button is not down after the board reset cycle is complete.

NOTE: Depressing the recovery button while the bootloader firmware is in its initial reset cycle stops the bootloader firmware from automatically transitioning back to the runtime firmware.

NOTE: The Ethernet connections will drop out for several seconds whenever the Spartan-6 is reloaded.

NOTE: It is easy to check which mode the board is in by inspecting the LEDs.

2.3 – Spartan-6 Board Identification

Communication with port 50000 can be used to identify information about the firmware running in the board. It can also be used to trigger a Spartan-6 firmware reload.

The interface is used by sending a single byte message to the port, with the following meanings:

0x01: Restart the Spartan-6 using the bootloader firmware.
0x81: Restart the Spartan-6 using the runtime firmware.
Any other value: Query the board identification information.

Sending any of the above values will produce the following response packet:

Byte 0: Identification format (currently ‘1’)
Byte 1: Board identification (1 == QF2-pre).
Byte 2: Active Spartan-6 firmware (0 == bootloader, 1 == runtime).
Bytes 3 – 6: Bootloader firmware build date.
Bytes 7 – 38: Bootloader firmware SHA256.
Bytes 39 – 44: Runtime firmware build date.
Bytes 45 – 76: Runtime firmware SHA256.
Bytes 77 – 148: Board unique identifier (UID).

The SHA256 values are generated from the Xilinx bitstream data (without the header), padded to the sector boundary of the PROM, to compensate for the fact that Spartan-6 bitstream sizes vary slightly in each build.

The board UID is hard-coded in the ATSHA204A device on the board, and is retrieved at powerup. It should be unique across all boards.

2.4 – Spartan-6 Configuration

The Spartan-6 configuration bus uses a simple 'write all registers + mask' process. While there are more complicated approaches, it's simple, synthesizes cleanly and is easy to understand. To write data values to the Spartan-6 registers, one sizes two blocks of bytes the size of the entire register space, then sets the values in one and the corresponding mask for the bits to change in the other. Sending the packet to 50001 will trigger a response packet containing the entire read-back register space, the network settings, and the write registers. In order to read the current board status, one sends a packet with the mask set to all zeros.

The register space stored in the PROM has the exact same format as the register space accessible via port 50001, with the addition of a network settings block which can only be changed by PROM configuration, and therefore requires a firmware reload to take effect.

The structure of the configuration interface varies between firmware revisions, but standard registers are referenced in the python using a string-based identifier. Standard registers are as follows:

2.4.1 - Network Settings

IPV4_UNICAST_IP_ADDRESS

Type: Integer String
Format: “XXX.XXX.XXX.XXX”
Default: 192.168.1.127
Description: IPv4 address of the board.

IPV4_UNICAST MAC

Type: Hex String
Format: “XX:XX:XX:XX:XX:XX”
Default: AA:BB:CC:DD:EE:FF
Description: MAC address of board.

IPV4_MULTICAST_MAC

Type: Hex String
Format: “XX:XX:XX:XX:XX:XX”
Default: 00:00:00:00:00:00 [DISABLED]
Description: IPv4 multicast MAC address to receive / send on.

IPV4_MULTICAST_IP

Type: Integer String
Format: “XXX.XXX.XXX.XXX”
Default: 0.0.0.0 [DISABLED]
Description: IPv4 multicast IP address to receive / send on.

IPV4_MULTICAST_PORT

Type: 16-bit Unsigned Integer
Default: 0 [DISABLED]
Description: IPv4 multicast port to receive / send on.

2.4.2 - Bootloader-Specific Settings

AUTOBOOT_TO_RUNTIME

Type: Bit
Default: 0
Description: If ‘1’, bootloader will automatically trigger a reload into the runtime image without waiting for an external command. Used for accessible systems where it’s preferable to complete startup without external intervention. Inaccessible systems should avoid enabling this bit.

2.4.3 - Runtime-Specific Settings

BOARD_SHUTDOWN_TEMPERATURE

Type: 8-bit Unsigned Integer
Default: 64
Description: PCB board temperature in degrees Celsius above which the main power is automatically turned off (including Kintex-7 and FMCs).

KINTEX_AUTOBOOT_SHA256

Type: Hex String
Format: “XXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXXX”
Default: “0000000000000000000000000000000000000000000000000000000000000000”
Description: SHA256 of Kintex-7 bitstream to load on startup. The Spartan-6 will look for this firmware in the PROM and load it if a matching firmware is found. It will not work if main power is not enabled as well.

KINTEX_SHUTDOWN_TEMPERATURE

Type: 8-bit Unsigned Integer
Default: 64
Description: Kintex-7 die temperature in degrees Celsius above which the main power is automatically turned off (including Kintex-7 and FMCs).

MAIN_POWER_ENABLE

Type: Bit
Default: 0
Description: Turns on / off main power on the board.

POWER_BURST_MODE

Type: Bit
Default: 1
Description: Controls whether the switch-mode supplies on the board are operated in burst mode (higher efficiency, higher noise & EMI) or synchronous mode (lower efficiency, lower noise & EMI).

NOTE: Burst mode is always enabled for the bootloader to lower power dissipation.

N_SI57X_A_CFG_ENABLE

Type: Bit
Default: 1
Description: Enables the configuration of SI57X_A. Set to ‘0’ to trigger an update / read of SI57X_A at startup.

SI57X_A_UPDATE

Type: Bit
Default: 1
Description: Used in concert with N_SI57X_A_CFG_ENABLE. When set to ‘1’, will copy the settings for HSDIV, N1, RFREQ into SI57X_A when the configuration is enabled. When set to ‘0’, N_SI57X_A_CFG_ENABLE will only trigger a read cycle and will not update the SI57X.

SI57X_A_OE

Type: Bit
Default: 0
Description: Output enable for SI57X_A.

SI57X_A_NEW_HSDIV

Type: 3-bit vector.
Default: 0
Description: New HSDIV value to load into SI57X_A.

SI57X_A_NEW_N1

Type: 7-bit vector.
Default: 3
Description: New N1 value to load into SI57X_A.

SI57X_A_NEW_RFREQ

Type: 38-bit vector.
Default: 0x02BBEAD49B
Description: New RFREQ value to load into SI57X_A.

N_SI57X_B_CFG_ENABLE

Type: Bit
Default: 1
Description: Enables the configuration of SI57X_B. Set to ‘0’ to trigger update / read of SI57X_B at startup.

SI57X_B_UPDATE

Type: Bit
Default: 1
Description: Used in concert with N_SI57X_B_CFG_ENABLE. When set to ‘1’, will copy the settings for HSDIV, N1, RFREQ into SI57X_B when the configuration is enabled. When set to ‘0’, N_SI57X_B_CFG_ENABLE will only trigger a read cycle and will not update the SI57X.

SI57X_B_OE

Type: Bit
Default: 0
Description: Output enable for SI57X_B.

SI57X_B_NEW_HSDIV

Type: 3-bit vector.
Default: 0
Description: New HSDIV value to load into SI57X_B.

SI57X_B_NEW_N1

Type: 7-bit vector.
Default: 3
Description: New N1 value to load into SI57X_B.

SI57X_B_NEW_RFREQ

Type: 38-bit vector.
Default: 0x02BBEAD49B
Description: New RFREQ value to load into SI57X_B.

2.4.4 - Common Settings

FAN_PWM_STOP_TEMPERATURE

Type: 8-bit Unsigned Integer
Default: 0
Description: Kintex-7 temperature in degrees Celsius below which the PWM control signal will be set to zero. This is only recommended for fans that support stop and start.

FAN_PWM_MINIMUM_TEMPERATURE

Type: 8-bit Unsigned Integer
Default: 40
Description: Kintex-7 temperature in degrees Celsius below which the PWM duty cycle will be fixed at FAN_PWM_MINIMUM_DUTY_CYCLE unless it also passes the stop threshold above.

FAN_PWM_MINIMUM_DUTY_CYCLE

Type: 8-bit Unsigned Integer
Default: 77
Description: Minimum allowed duty cycle, expressed as this numerator with a denominator of 255, i.e. 77 / 255 => ~30%. Some fans can tolerate a lower minimum, but the ATX standard requires a minimum of no more than 30%.

FAN_PWM_GRADIENT

Type: 8-bit Unsigned Integer
Default: 9
Description: Gradient of increase in the duty cycle, expressed as above per units of degrees Centigrade.

FAN_PWM_CURRENT_DUTY_CYCLE = FAN_PWM_MINIMUM_DUTY_CYCLE + FAN_PWM_GRADIENT * (KINTEX_7_TEMPERATURE – FAN_PWM_MINIMUM_TEMPERATURE).

The default will lead to a 100% duty cycle if the Kintex-7 passes approximately 60C.

MONITORING ENABLE

Type: Bit
Default: 0
Description: Turns on / off monitoring on the board.

SYS_I2C_RESET

Type: Bit
Default: 1
Description: Debug override pin for system I2C bus. Should not be modified under normal use.

SYS_I2C_SCL

Type: Bit
Default: 1
Description: Debug override pin for system I2C bus. Should not be modified under normal use.

SYS_I2C_SDA

Type: Bit
Default: 1
Description: Debug override pin for system I2C bus. Should not be modified under normal use.

N_TAS_2505_RESET

Type: Bit
Default: 0
Description: Reset control for TAS2505 audio amplifier. Should not be modified under normal use.

3.0 – Software and Firmware

3.1 – Getting the Latest Version

You can go here to get the latest tagged release of tools, firmware and examples:

https://gitlab.com/qf2-pre/users/tags

The latest release version can be downloaded as an archive or with git.

3.2 - Python Tools

The Python tools provide a comprehensive set of interface scripts for programming and configuring and the board. They are provided as a package, and as such are executed in from the top level of the user project, as:

python -m qf2_python.scripts.[NAME_OF_SCRIPT]

Specific scripts are described below.

add_kintex_7_image

Programs a Kintex-7 image into the PROM. Adds an entry to the Kintex-7 image table after verification.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-b [BITFILE]: Name of bitfile to download into PROM.

-v: Verbose diagnostic output (default == not verbose).

disable_main_power

Disables main power, including the Kintex-7 and FMCs.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-v: Verbose diagnostic output (default == not verbose).

enable_main_power

Disables main power, including the Kintex-7 and FMCs.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-v: Verbose diagnostic output (default == not verbose).

erase_kintex_7_image

Erases a Kintex-7 image from the PROM. It does this by removing the entry for the image from the image table.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-s [HASH]: SHA256 identifier hash for the bitstream.

-v: Verbose diagnostic output (default == not verbose).

erase_kintex_7_image_table

Erases the entire Kintex-7 image table.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-v: Verbose diagnostic output (default == not verbose).

get_board_information

Outputs information on board type & firmware.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-v: Verbose diagnostic output (default == not verbose).

get_board_interface

Tries to find a matching software interface for the board & firmware.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-v: Verbose diagnostic output (default == not verbose).

list_kintex_7_images

Displays all the Kintex-7 images in the PROM.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-v: Verbose diagnostic output (default == not verbose).

program_kintex_7

Streams a new Kintex-7 firmware into the FPGA over ethernet. Bypasses PROM.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-b [BITFILE]: Name of bitfile to load into Kintex-7 FPGA.

-v: Verbose diagnostic output (default == not verbose).

read_board_monitors

Demonstrates reading the board monitors on the board in a continuous loop.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-v: Verbose diagnostic output (default == not verbose).

read_fmc_prom

Example script demonstrating read / write of FMC PROMs over I2C.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-v: Verbose diagnostic output (default == not verbose).

read_qsfps

Example script demonstrating read / write of Kintex-7 QSFPs over I2C.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-v: Verbose diagnostic output (default == not verbose).

reboot_to_bootloader

Triggers a firmware reload to the bootloader firmware.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-v: Verbose diagnostic output (default == not verbose).

NOTE: This does not change the AUTOBOOT_TO_RUNTIME setting, so the bootloader will jump back to the runtime again if it is enabled.

reboot_to_runtime

Triggers a firmware reload to the runtime firmware.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-v: Verbose diagnostic output (default == not verbose).

udp_loopback_test

Sends variable-length packets over UDP and verifies the echo packet matches the one that was sent.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-p [PORT]: Port to target for loopback (default == 7).

update_spartan_6_configuration

Modifies the non-volatile Spartan-6 configuration in the PROM.

It begins by initializing a configuration space that matches the bitstream in the PROM. The tools will then read the PROM and verify the integrity of the non-volatile configuration. If the PROM is corrupted, the configuration space will carry its default settings. If the PROM settings are valid, they are copied into the configuration space.

The settings are then modified using a JSON input file and / or a settings argument list. Arguments that can be edited can be checked using verify_spartan_6_configuration first. Integers can be written in hexadecimal in the JSON file by quoting the number as a string and putting “0x” at the beginning. Integers on the command line must be provided in decimal.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

[FUTURE FEATURE] -l: Unlock PROM space before write, and lock again afterwards (default == disabled).

-X: Store the bootloader configuration (default == store the runtime configuration).

-d: Ignore PROM and force back to default settings (default == update PROM with overlay).

-r: Reboot the board automatically and verify restart after programming (default == no reboot).

-s, --settings: Settings to change. Provided as a key-value pair e.g. ‘SYS_I2C_SCL=1 SYS_I2C_SDA=2 IPV4_UNICAST_IP=192.168.1.127’

-p: JTAG access port (default == 50003).

-j: JSON settings file to use. Flat JSON format expected.

-v: Verbose diagnostic output (default == not verbose).

NOTE: The new settings will not take effect without a reboot.

NOTE: If you use ‘-r’ and have changed the network settings, the restart verification may fail if you have e.g. changed the board to a different MAC address.

update_spartan_6_image

Updates the Spartan-6 firmware image in the PROM. Also embeds an SHA256 hash of the bitstream and a storage and build date stamp after the bitstream itself. The new image can be activated by power cycling the board, using the recovery mode button, or a software reboot via port 50000. It can also be triggered using the ‘-r’ argument.

From version v0.59_unstable, this scans the configuration settings from the previous firmware by default and migrates them to the new firmware. Only firmwares from v0.58_unstable onward are recognized.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-b [BITFILE]: Name of bitfile to download into PROM (default == from firmware folder).

-f: Force firmware update even if currently stored firmware appears corrupt (default == no update).

-r: Reboot the board automatically and verify restart after programming (default == no reboot).

-n: Ignore changes to the configuration space when updating the firmware (default == update configuration space at the same time).

-v: Verbose diagnostic output (default == not verbose).

-p: JTAG access port (default == 50003).

-X: Program the bootloader image (default == program the runtime image).

NOTE: The hash of the bitstream is calculated from the bitstream padded to the PROM sector boundary. It is not the same as the hash of the bitfile.

verify_spartan_6_configuration

Downloads the current Spartan-6 configuration, verifies checksum, and displays current settings.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-b [BITFILE]: Name of bitfile to compare with PROM.

-X: Verify the bootloader configuration (default == verify the runtime configuration).

-p: JTAG access port (default == 50003).

-v: Verbose diagnostic output (default == not verbose).

verify_spartan_6_image

Verifies the current Spartan-6 firmware image in the PROM.

If a comparative bitfile isn’t provided, this will instead scan the stored bitstream and verify the SHA256 of that data matches the SHA256 stored after the bitstream.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

-b [BITFILE]: Name of bitfile to compare with PROM (default == integrity check).

-X: Verify the bootloader image (default == verify the runtime image).

-v: Verbose diagnostic output (default == not verbose).

-p: JTAG access port (default == 50003).

xilinx_virtual_cable

Implements a Xilinx Virtual Cable (XVC) interface that can be used by the Xilinx tools to interface with the Kintex-7 FPGA over ethernet without using a separate programming cable.

In Vivado, connection to this service can be done by running the following commands in the Vivado Hardware Manager Tcl console:

connect_hw_server
open_hw_target -xvc_url 127.0.0.1:2542

NOTE: If you have trouble getting this to work, make sure there is no hardware USB / JTAG pod connected to the computer running the tools and script. Vivado can become confused if multiple interfaces are available or multiple hardware servers are running.

NOTE: The other scripts listed here should not be used at the same time as this one.

Arguments:

-t [TARGET]: IP address of board to communicated with (default == 192.168.1.127).

[FUTURE FEATURE] 3.4 – Kintex-7 Firmware

Example firmware modules for the Kintex-7 are described below. They can be used as a starting point for application development, and are provided ‘as-is’ without any guarantee of behavior. They are designed to be compatible with the latest version of the Spartan-6 runtime. Build scripts for both ISE and Vivado are provided.
Appendix A – Recovering a Corrupted Bootloader

In the rare event that the bootloader is corrupted and you cannot communicate with the Spartan-6, the board has a standard Xilinx JTAG connector that is directly connected to the FPGA. The procedure to recover is:

- Reprogram the Spartan-6 using the bootloader firmware image using a JTAG programming cable attached to the header on the board (near the Ethernet).
- Verify the LEDs operate as expected – it should be noted that the firmware will still look at the PROM configuration settings upon startup, so you may wish to hold the recovery button down while programming the FPGA to force the firmware to use the default settings.
- Use the Python tools to reload the bootloader image into the PROM and the corresponding bootloader network settings. It is recommended to also verify the runtime image and configuration are as expected.

NOTE: Do NOT use the Xilinx tools to program the PROM. They do not fully support the PROMs or understand the data structure and will cause further corruption.